## Slide 1: Hydrothermal Plume Dispersion at Endeavour Segment: Modeling and Observations from Expedition AT50-15 (Aug 24th-Sept 17th, 2023) Guangyu Xu1, Chris German2, Victoria Preston3, Andrew Branch4, Mary Burkitt-Gray2, Rudi Lien5 1APL-UW, 2WHOI, 3Olin College, 4JPL-NASA, 5University of Oregon
Illustration by Natalie Renier (WHOI)

## Slide 2: Hydrothermal Estuaries: What sets the flux of hydrothermal Fe & Mn to the Deep Ocean Interior?
CTD Yo-Yos at MEF and High Rise:
  plume heights
  Survey depth
Numerical modeling:
  plume dispersion forecasts
AUV Sentry:
  plume surveys, in-situ sampling
Collection of water samples
  Standard shipboard CTD
  Specialized trace-metal CTD.
ONC mooring data:
  model validation
  real-time near-field dispersion directions
Spatial Scale:
< 100 km
Hydrothermal Estuary
Illustration by Natalie Renier (WHOI)

## Slide 3: Plume Height Observations from CTD YoYo Cast at High Rise Duration: ~ 13 hours; Start Time: 10 AM UTC on Aug 31st, 2023; Source Depth: 2176 m:
Max Height:
> 300 m
Neutrally buoyant plume fluid is ‘spicier’ (warmer and saltier) than seawater

## Slide 4: Numerical Modeling for Plume Dispersion Forecasts
Model: Regional Ocean Modeling System (ROMS).
Model forcing:
  Lateral boundaries:
    Non-Tidal: Global Ocean Physics Analysis and Forecast ( daily averages ) (https://doi.org/10.48670/moi-00016)
    Tidal: TPXO global tidal solution (Egbert and Erofeeva, 2002)
  Surface: ECMWF Forecasts
  Horizontal Resolutions: ~ 80 m
  Vertical Resolution: 64 layers, ~7 m near ridge crest
52 km
66 km

## Slide 5: Modeling of Hydrothermal Venting
ONC Moorings
Bottom Heat Sources:
  Area: 3 by 3 cells, ~ 240 m by 240 m
  Heat transfer rate:
    135 MW ( Mothra ) ( Kellog 2011 )
    1500 MW ( MEF )
    1800 MW ( High Rise )
    68 MW ( Salty Dawg ) ( Kellog 2011 )
    4.5 MW ( Sasquatch ) ( Kellog 2011 )
  Heat transfers at MEF and High Rise determined from model-observation matching.
    Likely overestimated due to model’s limitations:
      Large, uniform plume source
      Hydrostatic approximation

## Slide 6: Plume Height at High Rise: Model – Observation Comparison
Neutrally buoyant plume fluid is ‘spicier’ (warmer and saltier) than seawater

## Slide 7: Flow Velocities at ONC RCM-SW: Model – Observation Comparison
50 mab
125 mab
200 mab
1.5 cm/s
Eastward
Northward
1.5 cm/s
1.5 cm/s
Data
Model
Data
Model
Data
Model
200 mab
Model
Data

## Slide 8: Simulated Plume Dispersion (Aug 26th to Sept 16, 2023)
Aug 30th
Sept 3rd
Sept 5th
Sept 8th

## Slide 9: AUV Based Plume Surveys ( 12-Sep-2023 )
Simulated plume trajectory generally match observations.
Simulated plume shows a southward deviation compared to AUV observations.
Discrepancy likely due to model's overestimation of southward flow velocities.
Sentry
Target Depth: 2000 m
Photo courtesy of NDSF
Depth:
2000 m
Observation
Model

## Slide 10: Dispersal of Plume Particles
MEF

## Slide 11: Acknowledgements
Atlantis AT50-15 crew members
Sentry team members
Photo by Chris German
Thank you, Sentry!!!